## Slide 1: Knowledgebase of Interatomic Models Application Programming Interface (KIM API)
This document describes how KIM Tests and Models written in different languages work together. A unified interface, tuned for the specific needs of atomistic simulations, is presented. This interface is based on the concept of “descriptor files”. A descriptor file specifies all iaiables and methods required for communication between a particular Model and a Test. A “KIM API object” is created, based on the descriptor files, that holds all arguments (variable/data and method pointers) needed for Test/Model interaction. A complete set of KIM API service routines are available for accessing the various pointers in the KIM API object.
Valeriu Smirichinski, Ryan S. Elliott and Ellad B. Tadmor
Dept. of Aerospace Engineering and Mechanics, University of Minnesota
September 2011
1
alpha version openkim-api package
Notes: 1

## Slide 2: Contents
KIM overview
  Barriers faced by molecular modelers
  Knowledgebase of Interatomic Models (KIM) is proposed to overcome the barriers
  KIM framework
  KIM repository: Models
  KIM repository: Tests
  KIM repository: KIM data
KIM API concept and implementation:
  The KIM API facilitates communication between Models and Tests
  The most challenging technical requirement is the need for multi-language support
  The KIM API is based on exchanging pointers to data and methods
  How can a Test know what type of input/output data is required by a Model? We have solved this problem by introducing the KIM API descriptor file
  The structure of a descriptor file
  Handling of Neighbor lists and Boundary Conditions – NBC methods
  Test/Model coupling: The Model’s initialization routine stores a pointer to the “compute” routine in the KIM API object
  Initialization of a KIM API object, setting and getting data-pointers can be done through the KIM service routines
  KIM installation: compilation, linking and running Tests
University of Minnesota
2
Notes: 2

## Slide 3: Contents (2)
  Appendix
  Every argument that needs to be communicated between Tests and Models must be in the descriptor file
  The KIM API directory structure
  Model and Test examples available in the current version of the KIM API
  The KIM API object is an array of base data elements. Each base data element can hold a pointer to any relevant data (scalar, array, method, etc.)
University of Minnesota
3
Notes: 3

## Slide 4
  KIM overview
University of Minnesota
4
Notes: 4

## Slide 5: KIM TEAM
  PIs
  Ellad Tadmor (U. Minnesota)
  Ryan Elliott (U. Minnesota)
  James Sethna (Cornell)
  Developers
  Valeriu Smirichinski (U. Minnesota)
  Daniel Karls (U. Minnesota)
  Mihir Khadilkar (Cornell)
  Alex Alemi (Cornell)
  John Crow (Silicon Life Sciences)
  Trevor Wenblom (Silicon Life Sciences)
University of Minnesota
5
  Advisory Board
  Graeme Ackland (U. Edinburgh)
  Michael Baskes (LANL)
  Chandler Becker (NIST)
  Noam Bernstein (NRL)
  Ioana Cozmuta (NASA)
  Karsten Jacobsen (Tech. U. Den.)
  Ronald Miller (Carleton)
  John Moriarty (LLNL)
  Sadasivan Shankar (Intel)
  Adri van Duin (Penn State)
  Gabriel Wainer (Carleton)
Notes: 5

## Slide 6: Molecular/atomistic simulations: tests and models
University of Minnesota
6
Tests
Test :a specific computer program which, when coupled with a suitable Model, calculates and returns a specific Prediction about a particular Configuration (or sequence of Configurations for dynamical properties).
Models
Model : Computer implementation representing a specific interaction between atoms, e.g. an interatomic potential or force field
Source: openkim.org
Notes: 6

## Slide 7: Types of molecular modelers
University of Minnesota
7
Developers
- Create new models
- Study materials physics and applications
- Create new knowledge
Very broadly speaking there are two types of molecular modelers:
Users
- Use models to study materials problems of
scientific/technological importance
- Build sophisticated simulations to extract
meaningful data
- Create new knowledge
Users
Developers
Notes: 7

## Slide 8: Barriers faced by molecular modelers
The difficulties faced by developers and users of interatomic
models include:
  No easy access to an extensive list of reliable reference data from experiments and first principles calculations for fitting.
  No easy access to implementations of existing models with known provenance and cross-language capability.
  No standardized tests for evaluating properties of molecular systems.
  No framework for evaluating the precision and transferability of models and therefore no rigorous guidelines for choosing an appropriate model for a given application.
University of Minnesota
8
Notes: 8

## Slide 9: Knowledgebase of Interatomic Models (KIM) is proposed to overcome the barriers
University of Minnesota
9
The Knowledgebase of Interatomic Models (KIM) project is based on a four-year NSF cyber-enabled discovery and innovation (CDI) grant. The KIM project is designed to overcome the barriers mentioned on the previous page. KIM has the following main objectives:
Development of an online open resource for standardized testing and long-term warehousing of interatomic models (potentials and force fields) and data.
Development of an application programming interface (API) standard for atomistic simulations, which will allow any interatomic model to work seamlessly with any atomistic simulation code.
Fostering the development of a quantitative theory of transferability of interatomic models to provide guidance for selecting application-appropriate models based on rigorous criteria, and error bounds on results.
Striving for the permanence of the KIM project, including development of a sustainability plan, and establishment of a long-term home for its content.
More information on KIM is available at the project website: http://openKIM.org
Notes: 9

## Slide 10: KIM framework
University of Minnesota
10
Repository
Processing pipeline
KIM
Web portal
External repositories
A web interface that will facilitate:
user upload and download of Tests, Models and Reference Data
searching and querying the repository
comparing and visualizing Predictions and Reference Data
recording user feedback (ranking and discussion forums)
A user-extendible database of
interatomic Models
standardized Tests (simulation codes)
Predictions (results from Model-Test couplings)
Reference Data (obtained from experiments and first principles calculations)
Processing Pipeline:
An automatic system for generating Predictions due to new Test or Model upload or changes:
detect viable Test-Model couplings
assign computational resources based on priority and dependencies
store results in Repository
requires an application programming interface (API) to be defined
Notes: 10

## Slide 11: KIM repository: Models
University of Minnesota
11
Models Tests Predictions Reference Data KIM API
Models
Model: Computer implementation representing a specific interaction between atoms, e.g. an interatomic potential or force field.
Model Format
  - Stand-alone Model (black box)
  Model Driver (e.g. Lennard-Jones )
  + Parameter Set (e.g. =10.4 meV, =0.34 nm)
Every model will have a unique KIM ID for referencing in papers.
Lennard-Jones (pair)
• Ar parameterization
• ...
⠇
Morse (pair)
• Cu parameterization
• ...
⠇
Born-Mayer (ionic pair)
⠇
Stillinger-Weber (3-bdy)
• Si parameterization
• ...
⠇
MGPT (4-body)
• Mo parameterization
• Ta parameterization
• ...
⠇
CHARMM/AMBER
⠇
EAM/Finnis-Sinclair/glue
⠇
MEAM
⠇
Tersoff
⠇
EDIP
Brenner
⠇
Bond-order potentials
⠇
ReaxFF
⠇
GAP
⠇
Notes: 11

## Slide 12: KIM repository: Tests
University of Minnesota
12
Models Tests Predictions Reference Data KIM API
Tests
Test: a specific computer program which when coupled with a suitable Model, possible including additional input, calculates and returns a specific Prediction about a particular Configuration (or sequence of Configurations for dynamical properties).
• Prediction of a Test will be a logical, scalar, tensor, graph, configuration or field, computed from a Test-Model coupling
• Popular codes (ddcMD, DL_POLY, GROMACS, GULP, iMD, LAMMPS, NAMD, SPaSM, etc.) can be included in a library of tools for writing Tests.
• Automatic test generation by linking to external repositories of first principles results.
Scalars
- lattice constants
- cohesive energy
- vacancy formation energy
- surface energy
- grain boundary energy
- vacancy migration barrier
- dislocation mobility
- peierls stress
- melting temperature
-...
Tensors
- stress
- elastic constants
...
Configurations
- dislocation core structure
- surface structure
- grain boundary structure
- nanocluster structure
...
Graph
- phonon spectrum
- cohesive energy vs volume
- energy along transition path
- radial distribution functions
...
Fields
- simulated TEM hi-res image
- gamma surface
…
Notes: 12

## Slide 13: KIM repository: KIM Data
University of Minnesota
13
Models Tests Predictions Reference Data KIM API
Predictions Reference Data
Data in KIM can either be
‣ a Prediction computed from a Test-Model coupling, or
‣ Reference Data computed by first principles or measured experimentally.
• Standardization of Data
- Identified in terms of a set of “descriptors” drawn from a standardized “dictionary”
(similar to that used in the Protein Data Bank project)
- Descriptors will be automatically generated when possible (for example, the “Space Group”
descriptor will be automatically generated for a given crystal structure).
• Data classes
- Logical (true/false result for a test, e.g. a given crystal phase is stable)
- Scalar or Tensor (lattice constant, cohesive energy, elastic constants...)
- Graphs (transition pathway energy, phonon spectrum, ...)
- Configurations (relaxed defect core, surface structure, ...)
- Fields (simulated hires TEM image, ...)
• Quality assurance
- Acceptance of only “publication quality” data enforced by KIM Editor
- “Data Provenance”
Notes: 13

## Slide 14
  KIM API concept and implementation
University of Minnesota
14
Notes: 14

## Slide 15: The KIM API facilitates communication between Models and Tests
Test #n: using potential
for the given configuration finds stresses
Requires: forces between each pair of neighboring atoms…
1
University of Minnesota
15
Test #1: using model find min. energy configuration…
Model #4: EAM potential with tabulated embedding function
Calculates: forces between each pair neighboring atoms …
Model #1: Lennard-Jones potential with cutoff….
Test calls the Model---therefore they should be linked together as one executable.
Input for Model
Results
Tests can be written in different languages
Models can be written in different languages
Users and developers will be able to download Tests and Models (from openkim.org) , then compile, link and run the resulting programs to produce new results.
Notes: 15

## Slide 16: The most challenging technical requirement is the need for multi-language support
? ? ? ? ? ? ?
Processing pipeline: sequence of actions
detect a viable Model/Test coupling
build (compile and link) Tests against Model
run probe-tests
assign computational resources
run full-scale Test against Model
analyze results …
store results in the repository
Need a simple interface : ideally just one argument per call
Source: KIM kickoff presentation
2
openKIM.org framework
Processing pipeline: an automatic system for generating predictions when Tests or Models are uploaded or changed.
Requirements:
Multilanguage support (C, C++, F77, FORTRAN 90, Python …)
A variety of data structures need to be accommodated: scalars, multidimensional arrays, variable size arrays, etc..
Speed & performance are very important
Standardized API, version tracking, etc…
?
University of Minnesota
16
Notes: 16

## Slide 17: The KIM API is based on exchanging pointers to data and methods
? ? ? ? ? ? ?
Data standard should accommodate every possible data set required for the model
3
KIM
API
Many languages link
Data
standard
Method flexibility and speed
Model
(server)
Test
(client)
Pointer to standard data
Pointer
Pointer
Single executable
University of Minnesota
17
Data and method pointers are packed in one object. The Interface consists of exchanging one pointer to the KIM API object between a Test and a Model
All languages naturally support pointers:
  FORTRAN (cray or 2003 standard)
  C/C++
  Java
  Python
Concept
Schematic of implementation
Notes: 17

## Slide 18: Using C-style pointer in Fortran
3.1
University of Minnesota
18
In order to implement the KIM API concept in a cross-language environment, all
languages have to work with C-style pointers.
FORTRAN 77 and Fortran 90/95 do not support C-style pointers directly, however
essentially all compilers support the `cray pointers' extension which provides this capability.
A cray pointer is an integer that can store a memory address. An example below shows the
general syntax and usage of a cray pointer in Fortran compared with C.
…
double precision :: y=10.0d0
double precision :: x
pointer (px,x)
…
px = loc(y)
print*,”x=“,x
…
…
double y=10.0;
double *x;
x = &y;
printf(“*x=%f \n”, *x);
…
Keyword pointer, followed by two arguments
px - is a pointer (analog double *x in C)
x - is a pointee
As soon as px holds an address, access to that address is done by pointee x
FORTRAN code
C code
Notes: 18

## Slide 19: How can a Test know what type of input/output data is required by a Model? We have solved this problem by introducing the KIM API descriptor file
4
University of Minnesota
19
####################################################################################################
MODEL_NAME := model_Ne_P_MLJ_NEIGH_PURE_H
SystemOfUnitsFix := fixed
####################################################################################################
SUPPORTED_ATOM/PARTICLES_TYPES:
# Symbol/name Type code
Ne spec 1
...
MODEL_INPUT:
# Name Type Unit SystemU/Scale Shape Requirements
numberOfAtoms integer*8 none none []
numberAtomTypes integer none none []
atomTypes integer none none [numberOfAtoms]
...
model_Ne_P_MLJ_NEIGH_PURE_H.kim
Note: full .kim file shown here can be found in MODELs/model_Ne_P_MLJ_NEIGH_PURE_H/
KIM API descriptor file defines all arguments that the model needs for computation including input and output arguments. Also on the test side, the .kim file defines what the Test can provide as input for the Model and what it expects from the Model as a result.
Tests and Models expose the required input/output arguments that will be communicated using the KIM API
Notes: 19

## Slide 20: Structure of descriptor file
5
University of Minnesota
20
Section lines
Brief description of Section lines
SUPPORTED_ATOM/PARTICLES_TYPES:
CONVENTIONS:
MODEL_INPUT:
MODEL_OUTPUT:
MODEL_PARAMETERS:
These lines identify logically distinct sections within the KIM descriptor file.
All lines following a Section line, up to the next Section line or end of the file, will be assigned to the indicated section.
These sections may occur in any order within a KIM descriptor file, however the order given here is recommended. A section line may only occur once within a KIM descriptor file.
Data lines
* Species Data lines
* Dummy Data lines
* Argument Data lines
These lines are used to specify the information that a Model (Test) will provide to and require from a Test (Model), as well as the conventions that the Model(Test) uses.
* Species Data lines – allow for the definition of atomic species by providing a symbol and an integer code. These lines are located in section SUPPORTED_ATOM/PARTICLES_TYPES.
* Dummy Data lines - this line type defines a convention that can be used to ensure that Models and Tests are able to work together, and should only be used within the CONVENTIONS section of the KIM descriptor file.
* Argument Data lines – the main KIM descriptor file line format, used within the MODEL_INPUT, MODEL_OUTPUT, and MODEL_PARAMETERS sections.
Brief description of Data lines
Model/Test name and system of units lines
MODEL_NAME:=model_Ar_P_Morse
SystemOfUnitsFix := fixed
Notes: 20

## Slide 21: Each argument line in the descriptor file describes an argument and its properties
MODEL_NAME := model_Ar_P_MLJ_F90
SystemOfUnitsFix := fixed
….
compute method none none []
MODEL_OUTPUT:
# Name Type Unit SystemU/Scale Shape requirements
energy real*8 energy standard []
energyPerAtom real*8 energy standard [numberOfAtoms] optional
….
5.1
University of Minnesota
21
MODELs/model_Ar_P_MLJ_F90.kim
The “requirements” field is only used in Model descriptor files. An empty field indicates that the argument is required. A value of “optional” indicates that the associated data will be computed only if the argument is in the Test’s descriptor file and if the Test explicitly requests it.
Method means a subroutine or function pointer
Physical dimensions
Type of data in computer representation
The name of an argument is its “key word”. By using key words, the KIM service routines can pack/unpack data pointers from the KIM API object. Key words are standardized as part of the KIM API.
The shape of an argument describes its array properties. It specifies the number and size (range) of indices. For example, [] means a scalar (zero-dimensional array), [numberOfAtoms] means a one-dimensional array and [numberOfAtoms,3] means a two-dimensional array of size numberOfAtoms x 3.
System of units: standard, SI, none
Note: detailed description of all Types value , Unit, SystemU/Scale can be found in the file KIM_API/standard.kim
All characters after a ‘#’ are ignored
(a comment field)
Notes: 21

## Slide 22: Specifying atom types – species data lines
5.2
University of Minnesota
22
...
###############################################
SUPPORTED_ATOM/PARTICLES_TYPES:
# Symbol/name Type code
Ar spec 1
###############################################...
Species data lines define the atom/particle types supported by the Test/Model and should only be used within the SUPPORTED_ATOM/PARTICLES_TYPES
section of the KIM descriptor file. Each line consists of three white-space separated (case sensitive) strings The three strings are as follows:
code: This is the integer that the Model uses internally
to identify the atom/particle type. The value specified
by a Test is ignored.
Type: This must be `spec'.
Name: This string gives a unique name to the atom/particle type. This name is checked against the standard list in `standard.kim'.
The KIM_API_get_listAtomTypes() service routine allows one to obtain a list of all atom species used by the model during runtime. Also the KIM_API_get_atypeCode() service routine allows one to get the atom species integer code (see KIMserviceDescription.txt).
MODELs/model_Ar_P_MLJ_F90.kim
Notes: 22

## Slide 23: In order to define “conventions” of test/model behavior, dummy data lines are reserved
University of Minnesota
23
##############################################
CONVENTIONS:
# Name Type
OneBasedLists dummy
Neigh_IterAccess dummy
Neigh_LocaAccess dummy
NEIGH-RVEC-F dummy
NEIGH-PURE-H dummy
...
A dummy data line defines a convention (or parameter), that can be used to ensure that Models and Tests are able to work together, and should only be used within the CONVENTIONS section of the KIM descriptor file. The line consists of two white-space separated (case sensitive) strings. The two strings, in order, are as follows:
Name: This string gives a unique name to the convention. This name is checked against the standard list in `standard.kim‘
Type: This must be `dummy'
KIM_API_allocate() has no effect on “dummy “ type arguments, because they are not “data pointer holders“.
For a detailed description of all dummy lines see the file KIM_API/standard.kim. Also see template files in DOCs/TEMPLATEs/.
5.3
DOCs/TEMPLATEs/model_El_P_Template.f.kim
Notes: 23

## Slide 24: Parameter arguments are used to publish/access internal parameters of a Model
University of Minnesota
24
MODEL_PARAMETERS:
# Name Type Unit SystemU/Scale Shape requirements
PARAM_FREE_sigma real*8 length standard []
PARAM_FREE_epsilon real*8 energy standard []
PARAM_FIXED_cutsq real*8 area standard []
...
The format for parameter arguments in a KIM descriptor file is the same as that for argument data types.
Two types of model parameters are allowed
1) PARAM_FIXED_XXXXXX - these should not be changed by the Test
2) PARAM_FREE_XXXXXX - these may be changed by the Test (which must then call the
Model's reinit() function to inform the model that its parameters have changed)
KIM_API_get_listParams() service routine will return a list of all parameters in the object during runtime (as an array of text strings).
KIM_API_get_listFreeParams() service routine will return a list of FREE parameters and
KIM_API_get_listFixedParams() will return a list of FIXED parameters (see KIMserviceDescription.txt)
Names of parameter arguments are not checked against standard.kim
5.4
model_Ar_P_MLJ_CLUSTER/model_Ar_P_MLJ_CLUSTER.kim
Notes: 24

## Slide 25: Handling of Neighbor lists and Boundary Conditions – NBC methods
University of Minnesota
25
Neighbor list ?
MI-ORTHO
PBC ?
Relative Pos. Vectors Rij ?
Yes
No
CLUSTER
MI-OPBC
NEIGH-RVEC
NEIGH-PURE
NEIGH-PURE-H
NEIGH-PURE-F
Model needs neighbor lists
NEIGH-RVEC-F
Model needs neighbor list and relative position vectors Rij=xj-xi
MI-OPBC-H
MI-OPBC-F
Minimum image orthogonal periodic boundary conditions:
model needs neighbor lists and box side lengths
Plain vanilla method:
Model needs only coordinates
Yes
No
No
Yes
Note: NBC stands for Neighbor lists and Boundary Conditions
6
Notes: 25

## Slide 26: Descriptions of the NBC methods
University of Minnesota
26
CLUSTER:
Receives the number of atoms and coordinates without additional information (such as neighbor lists or other boundary condition specifiers) and computes requested quantities under the assumption that the atoms form an isolated cluster. For example, if energy and forces are requested, it will compute the total energy of all the atoms based on the supplied atom coordinates and the derivative of the total energy with respect to the positions of the atoms.
MI-OPBC-[F|H]:
Receives the number of atoms and coordinates, the side lengths for the periodic orthogonal box and a neighbor list as detailed below. Assumes all atoms lie inside the periodic box. Side lengths of box must be at least twice the cutoff range. Computes the requested quantities under the assumption that the atoms are subjected to minimum image, orthogonal, periodic boundary conditions.
Neighbor list requirements for MI-OPBC-[F|H]:
The minimum image convention is applied during construction of the neighbor list consistent with the orthogonal box size.
The neighbor list can be supplied in either full or half mode.
Full neighbor list: All neighbors of an atom are stored
Half neighbor list: For an atom i only the neighbors j>i are stored.
Calculated quantities for both –H and –F modes should be equivalent to those obtained were the model to compute its own neighbor list using the provided orthogonal periodic box side lengths.
6.1
Notes: 26

## Slide 27: Descriptions of the NBC methods (2)
University of Minnesota
27
NEIGH-PURE-[F|H]:
Receives the number of atoms, coordinates and a full or half neighbor list. The neighbor list defines the environment of each atom, from which the atom’s energy is defined. The model computes the requested quantities using the supplied information. For example, if energy and forces are requested, it will compute the total energy of all the atoms based on their neighbor lists and the derivative of the total energy with respect to the positions of the atoms. This method can be used with codes that use ghost atoms to apply boundary conditions. The ghost atoms are treated as regular atoms by the model, and it is up to the calling code to discard some information such as the forces on the ghost atoms and to compute the appropriate total energy from per-atom energies of the physical atoms, or to use a modified neighbor list to obtain the desired values.
NEIGH-RVEC-F:
Receives the number of atoms and coordinates, a full neighbor list and the relative position vectors Rij (Rij = xj-xi). The neighbor list and Rij vectors define the environment of each atom, from which the atom’s energy is defined. The model computes the requested quantities using the supplied information. For example, if energy and forces are requested, it will compute the total energy of all the atoms based on their neighbor lists and relative position vectors and the derivative of the total energy with respect to the positions of the atoms. This method enables the application of general periodic boundary conditions, including multiple images. (This approach can fail with half neighbor lists and therefore the –H variant of the method does not exist.) A possible future extension to this method is to allow the Test to provide a ForceTransformation() function for each neighbor, which would enable the application of complex boundary conditions such as torsion and objective boundary conditions.
6.2
Notes: 27

## Slide 28: Example of using NBC methods in KIM file
University of Minnesota
28
…
CONVENTIONS:
# Name Type
OneBasedLists dummy
NEIGH-RVEC-F
NEIGH-PURE-H dummy
NEIGH-PURE-F dummy
...
CLUSTER dummy
...
The template example in model_El_P_Template.f.kim
is designed to work with five different NBC methods.
If the Test can also work with multiple NBC methods and there are several matches, the first matched method listed in the Model’s KIM file will have precedence.
The KIM_API_init () routine will check that all needed lines for the chosen method are in KIM descriptor file.
NBC Methods
6.3
DOCs/TEMPLATEs/model_El_P_Template.f.kim
Notes: 28

## Slide 29: Neighbor list access methods: all related lines in KIM descriptor files
University of Minnesota
29
…
CONVENTIONS:
# Name Type
…
ZeroBasedLists dummy # presence of this line indicates that indexes
# for atoms are from 0 to numberOfAtoms-1 (C-style)
OneBasedLists dummy # presence of this line indicates that indexes for
# atoms are from 1 to numberOfAtoms (Fortran-style)
Neigh_IterAccess dummy # works with iterator mode
Neigh_LocaAccess dummy # works with locator mode
Neigh_BothAccess dummy # needs both locator and iterator modes
MI-OPBC-H dummy
MI-OPBC-F dummy
NEIGH-RVEC-F dummy
NEIGH-PURE-H dummy
NEIGH-PURE-F dummy
MODEL_INPUT:
# Name Type Unit SystemU/Scale Shape requirements
get_full_neigh method none none []
get_half_neigh method none none []
neighObject pointer none none []
boxlength real*8 length unspecified [3]
standard.kim (only related to Neighbor list access are shown here)
neighObject stores completely encapsulated neighbor list object
Access to the object is done through methods get_full_neigh or get_half_neigh . The neighbor list object and the method to access it are supplied by the Test.
6.4
Notes: 29

## Slide 30: Interface to methods: get_half_neigh & get_full_neigh
University of Minnesota
30
integer function get_half_neigh(pkim,mode,request,atom,numnei,pnei1atom,pRij)
implicit none
integer(kind=kim_intptr), intent(in) :: pkim
integer, intent(in) :: mode
integer, intent(in) :: request
integer, intent(out) :: atom
integer, intent(out) :: numnei
integer, intent(out) :: pnei1atom
integer, :: nei1atom(1); pointer(pnei1atom,nei1atom)
double precision, intent(out) :: pRij
double precision, :: Rij(3,*); pointer(pRij,Rij)
end function get_half_neigh
get_half_neigh and get _full_neigh functions both have the same interface
here :
mode - operate in iterator or locator
mode
mode = 0 : iterator mode
mode = 1 : locator mode
request - Requested operation
If mode = 0
request = 0 : reset iterator
request = 1 : increment iterator
If mode = 1
request = # : number of the atom
whose neighbor list
is requested
int get_half_neigh(void ** pkim, int * mode, int * request, int * atom,
int * numnei, int ** pnei1atom, double ** pRij) ;
FORTRAN style
C style
atom - the number of the atom whose neighbor list is returned
numnei - number of neighbors returned
nei1atom - integer array of neighbors of an atom which will point to
the list of neighbors on exit.
Rij - array of relative position vectors of the neighbors of an
atom (including boundary conditions if applied) if they
have been computed (NBC scenario NEIGH-RVEC-F
only). Has NULL value otherwise (all other NBC
scenarios).
The return value depends on the results of execution.
(see KIM_API/KIMserviceDescription.txt for details)
Test must supply the get_half/full_neigh method and store a pointer to it in the KIM API object
6.5
Notes: 30

## Slide 31: Model_init places compute method pointer in KIM API object
7
University of Minnesota
31
Test
free the KIM API object
Model
Initialize the KIM API object
Kim_api_init(pkim,test,model)
3. model_compute: unpack/get pointers to data, then perform computation.
Set (get) pointers to data, methods and objects or call KIM_API_allocate(…)
Change model parameters if necessary
Call KIM_API_model_reinit (…)
Use the Model’s compute method
KIM_API_model_compute(…)
4. model_destroy routine
(if necessary)
Pointer to KIM API object is the main argument communicated between Tests and Models
1. model_init, place compute method pointer into KIM API object
2. model_reinit, if parameters of the model have been changed
deallocate the Model
Call the model_init routine
Notes: 31

## Slide 32: Initialization of KIM API object, setting and getting data-pointers can be done through the KIM service routines
8
University of Minnesota
32
#include <stdint.h>
#ifdef __cplusplus
extern "C" {
#endif
//global methods
int KIM_API_init(void * kimmdl, char * testname, char *mdlname);
void KIM_API_allocate(void *kimmdl, intptr_t natoms, int ntypes);
void KIM_API_free(void *kimmdl, int * kimerror);
void KIM_API_print(void *kimmdl, int *kimerror);
void KIM_API_model_compute(void * kimmdl,int *kimerror);
…
//element access methods
int KIM_API_set_data(void *kimmdl,char *nm, intptr_t size, void *dt);
void * KIM_API_get_data(void *kimmdl,char *nm, int * kimerror);
…
KIMserviceC.h
Description of all KIM API service routines are located in the file:
KIM_API/KIMserviceDescription.txt
Directly place data pointer into the KIM API object
One can use optional KIM service routine to allocate standard arguments and data
Initialization is done by analyzing test and model descriptor files
Call model_compute routine by address stored in KIM API object
Notes: 32

## Slide 33: Examples of using KIM_API_init and KIM_API_allocate service routines
University of Minnesota
33
...
! Initialize the KIM object
ier = kim_api_init_f(pkim, testname, modelname)
if (ier.lt.KIM_STATUS_OK) then
call report_error(__LINE__, "kim_api_init_f", ier)
stop
endif
! Allocate memory via the KIM system
call kim_api_allocate_f(pkim, N, ATypes, ier)
if (ier.lt.KIM_STATUS_OK) then
call report_error(__LINE__, "kim_api_allocate_f", ier)
stop
endif
...
test_Ar_free_cluster_CLUSTER/test_Ar_free_cluster_CLUSTER.F90
KIM API init will check the consistency of KIM descriptor file (Test and Model) against standard.kim, after that will check if Test and Model match: NBC methods, atom species (if any) , conventions and argument data lines
If the match is successful, then the KIM API object is created. This object conforms to the Model descriptor KIM file and can store all described data as pointers
...
status = KIM_API_init(&pkim_periodic_model_0, testname, argv[1]);
if (KIM_STATUS_OK > status)
report_error(__LINE__,"KIM_API_init() for MODEL_ZERO for periodic",status);
...
test_Ar_multiple_models/test_Ar_multiple_models.c
KIM_API_allocate will allocate memory for all arguments stored in the KIM API object
It is not mandatory to use
KIM_ API_allocate. A Test can use its own memory and set address of the data in the KIM API object.
8.1
Notes: 33

## Slide 34: Examples of using KIM API get/set data
University of Minnesota
34
...
integer(kind=8) numberOfAtoms;
pointer(pnAtoms,numberOfAtoms)
...
! Unpack data from KIM object
!
pnAtoms = kim_api_get_data_f(pkim, "numberOfAtoms", ier);
if (ier.lt.KIM_STATUS_OK) then
call report_error(__LINE__, "kim_api_get_data_f", ier)
stop
endif
...
test_Ar_free_cluster_CLUSTER/test_Ar_free_cluster_CLUSTER.F90
...
/* Register memory */
/* model inputs */
status = KIM_API_set_data(pkim_periodic_model_0, "numberOfAtoms", 1, &numberOfAtoms_periodic);
if (KIM_STATUS_OK != status) report_error(__LINE__,"set data",status);
status = KIM_API_set_data(pkim_periodic_model_1, "numberOfAtoms", 1, &numberOfAtoms_periodic);
if (KIM_STATUS_OK != status) report_error(__LINE__,"set data",status);
...
KIM_API_get_data (or kim_api_get_data_f) will return address of data stored in the KIM API object.
ier will be equal 1 upon successful completion, otherwise it will be 0 or negative
(see KIM_API/KIMserviceDescription.txt)
KIM_API_set_data (or kim_api_set_data_f) will place the address of data into KIM API object and will return integer error code : 1– success, 0 or negative – unsuccessful completion
8.2
test_Ar_multiple_models/test_Ar_multiple_models.c
Notes: 34

## Slide 35: KIM_API_model_init will call model initialize routine that in turn will place model compute into KIM object
University of Minnesota
35
...
/* call model init routines */
status = KIM_API_model_init(pkim_periodic_model_0);
if (KIM_STATUS_OK != status) report_error(__LINE__, "KIM_API_model_init", status);
...
/* call compute functions */
KIM_API_model_compute(pkim_periodic_model_0, &status);
if (KIM_STATUS_OK != status) report_error(__LINE__, "compute", status);
...
...
subroutine model_<FILL element name>_P_<FILL model name>_init(pkim)
...
! store pointer to compute function in KIM object
ier = kim_api_set_data_f(pkim,"compute",one,loc(Compute_Energy_Forces))
if (ier.ne.KIM_STATUS_OK)&
stop '* ERROR: compute keyword not found in KIM object.'
...
DOCs/TEMPLATEs/model_El_P_Template.F90
KIM_API_model_init will call the model_init routine . KIM_API_model_init utilizes the KIM standard naming convention in order to make the call. In C the name of the model init routine must have all lower case letters in the following format modelname_init_, for example:
model_ar_p_mlj_cluster_init_
model name
KIM_API_model_compute calls the address of the model compute subroutine stored in KIM API object.
By the time KIM_API_model_compute is called the address is placed in KIM API object by model_init_ routine
Place address of actual compute routine into the KIM API object
8.3
test_Ar_multiple_models/test_Ar_multiple_models.c
Notes: 35

## Slide 36: An example of using get_half/full_neigh methods through KIM API service routines
...
do i = 1,numberOfAtoms
! Get neighbors for atom i
!
atom = i ! request neighbors for atom i
if (HalfOrFull.eq.1) then
ier = kim_api_get_half_neigh_f(pkim,1,atom,atom_ret,numnei, &
pnei1atom,pRij_dummy)
else
ier = kim_api_get_full_neigh_f(pkim,1,atom,atom_ret,numnei, &
pnei1atom,pRij_dummy)
endif
if (ier.lt.KIM_STATUS_OK) then
call report_error(__LINE__, "kim_api_get_*_neigh", ier)
return
endif
! Loop over the neighbors of atom i
!
do jj = 1, numnei
j = nei1atom(jj)
Rij(:) = coor(:,j) - coor(:,i) ! distance vector between i j
Rsqij = dot_product(Rij,Rij) ! compute square distance
if ( Rsqij < model_cutsq ) then ! particles are interacting?
r = sqrt(Rsqij) ! compute distance
call pair(model_epsilon,model_sigma,model_A,model_B, &
model_C, r,phi,dphi,d2phi) ! compute pair potential
...
University of Minnesota
36
MODELs/ model_Ar_P_MLJ_NEIGH_PURE_H_F/ model_Ar_P_MLJ_NEIGH_PURE_H_F.F90
Locator mode -- get neighbors of an atom using half or full neighbor lists as requested.
KIM_API_get_half/full_neigh will call the method using the address stored in the KIM API object (“get_half_neigh” or “get_full_neigh”). These methods are supplied by the Test.
KIM_API_get_half/full_neigh will check if the arguments are set correctly. It will also convert the result from oneBaseLists to zeroBaseLists (or vice versa) if necessary .
Details on the interface and a description of error codes are in
DOCs/KIMserviceDescription.txt
8.4
Notes: 36

## Slide 37
  Appendix
University of Minnesota
37
Notes: 37

## Slide 38: Every argument that needs to be communicated between tests and models must be in the descriptor file
University of Minnesota
38
Each Test has its own descriptor file that describes the data it can supply to the Model and what data it expects the Model to compute. There are no optional arguments in a Test’s descriptor file (because the test knows, a priori, what it will need to compute).
Each Model has its own descriptor file that describes the data it needs to perform its computations and what results it can compute. Some of the arguments/methods can be identified as optional. Optional arguments/methods are ones that the Test does not have to provide or are results that the Model will only compute if the Test explicitly requests it.
KIM service routines (such as kim_api_init_) use both Test and Model descriptor files to:
Check if the Model and Test match, also check if their descriptor files conform to the KIM API standard
If they do -- create a KIM API object to store all arguments described in the Model’s descriptor file
Mark each optional argument that is not used by the Test “uncompute” (i.e., do not compute)
Other service routines are used to:
Set (get) argument or method pointers into (from) the KIM API object
(e.g., kim_api_set_data, kim_api_get_data, etc.)
Check if the “compute flag” is set to “compute” for an argument in the KIM_API obejct
(kim_api_isit_compute)
Execute the Model’s compute method (kim_api_model_compute)
etc…
A1
Notes: 38

## Slide 39: Model and Test examples available in the current version of KIM API
University of Minnesota
39
test_Al_FCCcohesive_MI_OPBC
test_Al_free_cluster
test_ArNe_B2cohesive_NEIGH_RVEC
test_Ar_FCCcohesiveCutoff_NEIGH_RVEC
test_Ar_FCCcohesive_MI_OPBC
test_Ar_FCCcohesive_NEIGH_PURE
test_Ar_FCCcohesive_NEIGH_RVEC
test_Ar_free_cluster
test_Ar_free_cluster_CLUSTER_C
test_Ar_free_cluster_CLUSTER_F90
test_Ar_multiple_models
test_Ne_free_cluster
TESTs
model_Al_PF_ErcolessiAdams
model_ArNe_P_MLJ_NEIGH_RVEC_F
model_Ar_P_LJ
model_Ar_P_MLJ_C
model_Ar_P_MLJ_CLUSTER_C
model_Ar_P_MLJ_CLUSTER_F90
model_Ar_P_MLJ_F90
model_Ar_P_MLJ_MI_OPBC_H_F
model_Ar_P_MLJ_NEIGH_PURE_H_F
model_Ar_P_MLJ_NEIGH_RVEC_F
model_Ar_P_Morse
model_Ne_P_LJ
model_Ne_P_LJ_NEIGH_PURE_H
model_Ne_P_MLJ_NEIGH_RVEC_F
model_Ne_P_Morse
MODELs
Indicates a Test can work (match) with a Model in the current KIM API version
A3
Description of the Models and Tests provided with the KIM API package are given in the files MODELs/EXAMPLES.README and TESTs/EXAMPLES.README.
Notes: 39

## Slide 40: KIM API directory structure
University of Minnesota
40
openkim-api-XX.XX.XX
KIM_API
MODELs
TESTs
KIMservice.h
KIMservise.cpp
KIMserviceC.h
KIMserviceC.c
KIMservice.F90
KIMstatus.h
…
Sample_01_lj_cutoff
Sample_01_lj_cutoff
Sample_01_lj_cutoff
Sample_01_lj_cutoff
model_Ar_P_MLJ_C
Sample_01_lj_cutoff
Sample_01_lj_cutoff
Sample_01_lj_cutoff
Sample_01_lj_cutoff
test_Al_free_cluster
Makefile
model_Ar_P_MLJ_C.kim
model_Ar_P_MLJ_C.c
Plus any other files
needed
…
Makefile
test_Al_free_cluster.kim
test_Al_free_cluster.F90
Plus any other files
needed
…
Each Test and Model has its own descriptor file
A2
MODEL_DRIVERs
Sample_01_lj_cutoff
Sample_01_lj_cutoff
Sample_01_lj_cutoff
Sample_01_lj_cutoff
model_driver_P_Morse
Makefile
model_driver_P_Morse.kim
model_driver_P_Morse.c
Plus any other files
needed
…
Notes: 40

## Slide 41: KIM API object is an array of Base data elements. Each Base data element can hold a pointer to any relevant data
Flag contains additional information (all fields are integers)
rank and shape:
rank is the number of indices for the array: for 2D it is 2, for 3D it is 3 etc…
shape is an integer array of size rank and holds the size (range) of each index.
University of Minnesota
41
Can hold any type of array: real, integer, pointer…
Stores enough information for a complete description of the data
Base data:
Number of fields is fixed to 9
Every field in the Base data structure is a pointer or “pointer size” integer.
Base data type can be used to store all needed data for Tests and Models
peratom
freeable
pointerchanged
ID
auxiliary array: very useful for 2d arrays (variable and fixed dimensions)
pointer to contiguous array of data of size “size”
name contains description information like “coordinates”, “velocities”, “forces”, etc…
type tells the type for elements of array: “real”, “real*8“integer”, “integer*8”, pointer
size of data in terms of underlying elements
A4
Notes: 41

## Slide 42
  The end
University of Minnesota
42
Notes: 42

## Slide 43: KIM installation: compilation, linking and running tests
University of Minnesota
43
Instructions for installing, compiling and linking KIM:
In the desired directory, execute the command: ‘tar xzvf openkim-api-XX.XX.XX.tgz’
Set up environment variable (bash):
> export KIM_DIR=/your_location/openkim-api/
your_location is the correct path where the openkim-api directory is located.
(Make sure to include the trailing slash)
By default, all make files use the GNU compilers for 64 bit linux.
In order to use the Intel compiler, define the environment variable KIM_INTEL
bash:
> export KIM_INTEL="yes".
For using a 32 bit machine, define the environment variable KIM_SYSTEM32
bash:
> export KIM_SYSTEM32="yes"
4. Change directory to EXAMPLES_LEGO type make: it will populate TESTs and MODELs directories with actual code.
4. change to the KIM_DIR directory and execute the commands:
‘make clean’
‘make’
This will compile the KIM API and examples in TESTs and MODELs.
To run a Test, change to the appropriate directory and run the executable. For example:
> cd TESTs/<test_name>
> echo “<model_name>" | ./<test_name>
Note: refer to openkim-api/INSTALL for details on environment variables and other features
Notes: 43